## Slide 1: USTM17 Linux Network Administration
Lesson 2: Introduction to Linux Networking
Peter CHUNG (cspeter@cse.ust.hk)

## Slide 2: Introduction to Networking
Network
  A collection of hosts that communicate with each other (wired or wireless)
  Hosts are often computers, but may also be other devices such as
    an intelligent printer
    a cell phone
    a scanner
    or even a smart toilet

## Slide 3: What are Network Protocols?
Protocols ≈ Human languages
  Communication among hosts
Network protocols
  HTTP, FTP, SMTP, IMAP, POP3, TCP, UDP….

## Slide 4: Types of networks
TCP/IP networks
  The most popular protocol suite on both Local Area Networks (LANs) and Wide Area Networks (WANs)
Other types of networks
  UUCP
    to transport news and mail over dialup telephone connections
  IPX
    used in the Novell Netware environment
  They are less common nowadays

## Slide 5: History of TCP/IP Networks
A research project funded by the United States Defense Advanced Research Projects Agency (DARPA) in 1969
Converted into an operational one in 1975
In 1983, the new protocol suite TCP/IP was adopted as a standard, and all hosts on the network were required to use it

## Slide 6: Applications related to TCP/IP networks
Applications we learned in this course
  Domain Name System (DNS)
  Directory Services – We will use OpenLDAP
  Network File System (NFS)
  Firewall
Other applications we may not be able to cover in this course
  Web Server
  FTP Server
  SMTP mail server

## Slide 7: Ethernet
The most common type of LAN hardware is known as Ethernet
Net transfer rate (in Mega bits per second: Mbps)
  Examples: 10Mbps, 100Mbps, 1,000Mbps, 1Gbps, 10Gbps….

## Slide 8: Other types of hardware
They are not commonly used nowadays
Fiber Distributed Data Interface (FDDI)
  Was considered an attractive campus backbone technology in the early to mid 1990s
  Full speed equal to 100Mbps and the maximum cable length can be up to 200km, which is much flexible than Thicknet and Thinnet
  Now, it is obsolete by fast Ethernet
IBM’s Token Ring network
  An older and quickly disappearing technology

## Slide 9: Thick Ethernet (10-Base5)
Use coaxial cable
Drill a small hole into the cable and attach a transceiver using a vampire tap
Features:
  Transfer rate: 10Mbps
  Cable can run for a maximum 500 meters
  Adding hosts to the thick Ethernet do not need to bring down the network

## Slide 10: Thin Ethernet (10-Base2)
Use coaxial cable
Differing in diameter
It uses T-shaped “BNC” connector
Features
  Transfer rate: 10Mbps
  Cable can run for at most 200 meters
  Have to cut the cable to insert the connector, need to disrupt the network

## Slide 11: Twisted Pair Ethernet (10-BaseT)
Unlike Thinknet and Thinnet, T refers to twisted pair cable
A cable consists of a pair of copper wires
Features
  A hub/switch is required to act as an interconnection point
  Hosts can be added without disrupting the network

## Slide 12: Why we need to twist the pair of wires?
Twisting two wires makes them less susceptible to electrical noise than leaving them parallel
12
Notes: 12

## Slide 13: Modern Ethernet Cables
When you are shopping for cables
  you may notice the names are “Cat-5,” “Cat-7a,” or something similar
  Both Cat 3 and Cat 5 Ethernet cables are obsolete
A general rule of thumb is that higher numbers represent faster speeds and higher frequencies
Shielding cables are covered with a layer of grounded foil that helps prevent electromagnetic interference
Common categories of Cables

## Slide 14: Repeaters, bridges and routers
Ethernet has a limited cable length
To extend the coverage of a Ethernet, several hardware components are designed
Repeaters
  Copy signals between two or more LAN segments so that all segments will act as if one single LAN
Bridges and Routers
  Smarter devices which are able to analyze and decide whether to forward the network packets
  Bridges are used inside the same subnet, while routers are used between subnets

## Slide 15: Network Interface Card (NIC)
A network interface card (NIC) is required to connect a modern Ethernet
A 6-byte (48-bits) unique hardware address is hardcoded in the NIC firmware
  It is named as MAC address
MAC address format
  Uses hexadecimal notation
  aa:bb:cc:dd:ee:ff

## Slide 16: A simple campus network
Two Ethernets (Maths Dept and Physics Dept),
both of them are connected to the campus backbone

## Slide 17: The Internet Protocol (IP)
In the previous example, two professors
  One from the Math Dept, one from the Physics Dept
  They would like to communicate to each other
  They are connected, but they are in two different LAN segments
  How can they communicate to each other?
Routing and Internet Protocol
  Routing
    Directing datagrams to a remote host
  Internet Protocols (IP)
    Defines how to communicate among different connected hosts, even they are not in the same LAN segment

## Slide 18: IP addressing
Each host is assigned a unique 32-bit number within the same network
IP address
  A hardware independent address
  Example:
    192.168.1.100
  We will talk more about IP addresses in the next lesson

## Slide 19: Dot decimal notation (for IPv4)
Why using dot decimal notation for IP addresses?
Dot decimal notation is used to represent this 32-bit number. For example:
  Binary notation: many zeros and ones! (Hard to read and write!)
  Hexadecimal notation: 0x954C0C04 (Hard)
  Decimal notation: 2504788996 (Hard)
  Dot decimal notation: 149.76.12.4 (Easy)

## Slide 20: Hostname resolution
Mapping a hostname into an IP address
Reasons
  Human can understand numbers, but they are not good at memorizing numbers
  Example: 185.199.108.153
  However, it is very hard to memorize these numbers and then type the numbers to a web browser
    For names, it is easier to remember (e.g. hkpeterpeter.github.com)
Example of hostname resolution
  hkpeterpeter.github.com  185.199.108.153

## Slide 21: Address resolution
Mapping a hardware independent IP address into a hardware dependent MAC address
The MAC address is hardcoded in the firmware of the network interface card (NIC)
Example of address resolution
  185.199.108.153  AD:5C:99:77:66:99

## Slide 22: TCP and UDP
Role of Internet Protocol (IP)
  Sending datagram from one host to a remote host using their IP addresses
  Several problems may appear during the transmission (e.g. packet loss, out-of-the-order packets)
Transport Layer Protocols
  Provides extra features on top of the IP
  Transmission Control Protocol (TCP)
  User Datagram Protocol (UDP)

## Slide 23: TCP and UDP
TCP
  Provides a reliable service on top of the IP
  Ports are introduced to distinguish between different processes (e.g. web server, FTP server) in the same machine
  IP addresses and ports are used to establish a connection
    It provides an illustration of a simple connection between two processes on your machine and the remote machine
UDP
  It also uses IP addresses and ports
  Doesn’t require us to establish a connection
  Not designed to deal with datagram loss, the datagram loss is handled by the application

## Slide 24: What are Ports?
Ports may be viewed as attachment points for network connection
To communicate, both the server side and the client side are required to have a port
Server
  Attaches itself to a port and waits for the clients indefinitely
  Server ports are usually well-known (e.g. port 80 is usually a web server)
Client
  Usually allocates a random port on a local machine and connects to the server port on the remote machine

## Slide 25: What are Ports?
IP: 192.168.1.100
IP: 192.168.1.133
Webpage access
Port: 26308 (random)
Port: 80 (fixed)
FTP session
Port: 26309 (random)
Port: 21 (fixed)

## Slide 26: Common port numbers and port number assignment
Common port numbers
  FTP data (port 20)
  FTP control message (port 21)
  SSH (port 22)
  SMTP (port 25)
  DNS (port 53)
  HTTP (port 80)
  HTTPS (port 443)
  Remote Desktop Protocol (port 3389)
Port number assignment
  Governed by Internet Engineering Task Force (IETF)
  Linux to store port number assignment
    /etc/services

## Slide 27: TCP ports and UDP ports
Both TCP and UDP connection reply on ports
These two port numbers do not conflict to each other
  TCP port 80 is different from UDP port 80
In most case, TCP port and UDP port will be assigned to the same service
Some outdated exceptions exist
  rlogin (TCP port 513)
  rwho (UDP port 513)

## Slide 28: Any questions so far?